## Slide 1: Introduction to Computer Science
Exercises

## Slide 2: (Q) computer and a calculator
  1. What is the most important difference between a computer and a calculator A calculator can only process numerical data, which means, it can only work with numbers, but a computer can process alphanumerical data, such as numbers, letters, graphics, pictures, video, audio files and much more. A calculator can only be programmed to calculate numbers. A computer can use thousands different programs.
  2. Name and describe three special-purpose input devices people commonly use in public places, such as stores, banks, and libraries. 1. A touch screens – used for entering commands and answering questions 2. A bar code reader – used for scanning product information, and a scale for security and accuracy 3. Credit card, or a library membership card reading device.

## Slide 3: (Q) Number: Conversion
  Convert 10010101 from two’s complement to its equivalent base ten form.
  Encode 13.5 into the floating-point representation

## Slide 4: (Q) Number: Conversion
Convert number
  (18)10 = ( )2
  (58)10 = ( )2
  (0.625)10 = ( )2
  (0.3125)10 = ( )2
  1101.1012 = ( )10
  (-12.25)10 = ( )2s complement
    Assume 6 bits for integer and 3 bits for fractional number.

## Slide 5: (A) Number: Conversion
Convert number
Use repetitive multiplication or division method
  (18)10 = 16 + 2 = 24 + 21 = (10010)2
  (58)10 = 32 + 16 + 8 + 2 = 25 + 24 + 23 + 21 = (111010)2
  (43)10 = (101011)2
  (0.625)10 = 0.5 + 0.125 = 2-1 + 2-3 = (0.101)2
  (0.3125)10 = (.0101)2
  1101.1012 = (123 + 122 + 120 + 12-1 + 12-3)10

## Slide 6: (Q) Number: BINARY to HEXADECIMAL
Convert numbers
  (10 111 011 001 . 101 110)2 = ( )8
  (2731.56)8 = ( )2
  (101 1101 1001 . 1011 1000)2 = ( )16
  (5D9.B8)16 = ( )2

## Slide 7: (A) Number: BINARY to HEXADECIMAL
Convert numbers
  Binary  Octal: partition in groups of 3
    (10 111 011 001 . 101 110)2 = (2731.56)8
  Octal  Binary: reverse
    (2731.56)8 = (010 111 011 001 . 101 110)2
  Binary  Hexadecimal: partition in groups of 4
    (101 1101 1001 . 1011 1000)2 = (5D9.B8)16
  Hexadecimal  Binary: reverse
    (5D9.B8)16 = (0101 1101 1001 . 1011 1000)2

## Slide 8: (Q) Number: Representation
For 4-bit system, fill in the table below
Positive values Negative values
Value | Sign-and-Magnitue | 1s Complement | 2s Complement
+7 |  |  | 
+6 |  |  | 
+5 |  |  | 
+4 |  |  | 
+3 |  |  | 
+2 |  |  | 
+1 |  |  | 
+0 | 0000 |  | 
Value | Sign-and-Magnitue | 1s Complement | 2s Complement
-0 |  |  | 
-1 |  |  | 
-2 |  |  | 
-3 |  |  | 
-4 |  |  | 
-5 |  |  | 
-6 |  |  | 
-7 |  |  | 
-8 |  |  | 

## Slide 9: (A) Number: Representation
For 4-bit system, fill in the table below
Positive values Negative values

## Slide 10: (Q) Number: 2s complement addition and subtraction
4-bit system
Which one is overflow? Why?
+3 0011
+ +4 + 0100
---- -------
+7 0111
---- -------
-2 1110
+ -6 + 1010
---- -------
-8 11000
---- -------
+6 0110
+ -3 + 1101
---- -------
+3 10011
---- -------
+4 0100
+ -7 + 1001
---- -------
-3 1101
---- -------
-3 1101
+ -6 + 1010
---- -------
-9 10111
---- -------
+5 0101
+ +6 + 0110
---- -------
+11 1011
---- -------
(a)
(b)
(c)
(d)
(e)
(f)

## Slide 11: (A) Number: 2s complement addition and subtraction
Algorithm for addition, A + B
  Perform binary addition on the two numbers.
  Ignore the carry out of the MSB.
  Check for overflow. Overflow occurs if the ‘carry in’ and ‘carry out’ of the MSB are different, or if result is opposite sign of A and B.
Algorithm for subtraction, A – B = A + (-B)
  Take 2s-complement of B.
  Add the 2s-complement of B to A.
Overflow
  If the result of addition/subtraction goes beyond this range, an overflow occurs.
  Overflow can be easily detected:
    positive add positive  negative
    negative add negative  positive
  Example: 4-bit 2s-complement system
    Range of value: -810 to 710
    01012s + 01102s = 10112s, 510 + 610 = -510 ?! (overflow!)
    10012s + 11012s = 101102s (discard end-carry) = 01102s , -710 + -310 = 610 ?! (overflow!)

## Slide 12: (A) Number: 2s complement addition and subtraction
4-bit system
Which one is overflow?
+3 0011
+ +4 + 0100
---- -------
+7 0111
---- -------
-2 1110
+ -6 + 1010
---- -------
-8 11000
---- -------
+6 0110
+ -3 + 1101
---- -------
+3 10011
---- -------
+4 0100
+ -7 + 1001
---- -------
-3 1101
---- -------
-3 1101
+ -6 + 1010
---- -------
-9 10111
---- -------
+5 0101
+ +6 + 0110
---- -------
+11 1011
---- -------
(a)
(b)
(c)
(d)
(e)
(f)
Overflow
Overflow

## Slide 13: (Q) Boolean algebra
  Prove the Boolean equation below.
      X(X+Y) = X
      (1) Derive the Boolean equation with the dual relationship
      (2) Simplify
  2. Prove the Boolean equation above using the truth table.

## Slide 14: (Q) Boolean Algebra
Simplify (x+y)(x+y')(x'+z)

## Slide 15: Exercises
Arithmetic
Digital logic
Architectures

## Slide 16: (Q) Sum-of-Product and NAND gates
Draw gate-level circuit. Use 2-level NAND and NOT gates.
  F = AB + C'D + E

## Slide 17: (Q) Karnaugh Map
Given sum-of-minterms formulation, draw Karnaugh map and obtain the simplified Boolean expression
F (w,x,y,z) = w'∙x∙y'∙z' + w'∙x∙y'∙z + w∙x'∙y∙z'
+ w∙x'∙y∙z + w∙x∙y∙z' + w∙x∙y∙z
=  m(4, 5, 10, 11, 14, 15)

## Slide 18: (Q) Karnaugh Map
An odd parity generator for BCD code which has 6 unused combinations. Derive Boolean expression for P.
A | B | C | D | P
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | X
1 | 0 | 1 | 1 | X
1 | 1 | 0 | 0 | X
1 | 1 | 0 | 1 | X
1 | 1 | 1 | 0 | X
1 | 1 | 1 | 1 | X

## Slide 19: (Q) Combinational Circuit: MUX
Draw truth table for 4-by-1 multiplexor
Design and draw the combinational logic using AND, OR, NOT gates
4:1mux
Y
Inputs
select
S1 S0
I0
I1
I2
I3

## Slide 20: Algorithm
The task is to find the roots of a quadratic equation: ax2+bx+c=0

## Slide 21: Algorithm
Given an array of n integers. The task is to find the largest number which is a perfect square. Print -1 if there is no number that is perfect square.
Input :
arr[] = {9, 20, 49, 5, 3, 6}
Output : 49
Explanation: 49 is the largest number that is a perfect square.

## Slide 22: Algorithm (Happy number)
A number is called happy if it leads to 1 after a sequence of steps where in each step number is replaced by sum of squares of its digit that is if we start with Happy Number and keep replacing it with digits square sum, we reach 1.
Input: n = 19
Output: True
19 is Happy Number,
1^2 + 9^2 = 82
8^2 + 2^2 = 68
6^2 + 8^2 = 100
1^2 + 0^2 + 0^2 = 1
As we reached to 1,
19 is a Happy Number.
Input: n = 20
Output: False
A number will not be a Happy Number when it makes a loop in its sequence that is it touches a number in sequence which already been touched. So to check whether a number is happy or not, we can keep a set, if same number occurs again we flag result as not happy.