## Slide 1: Introduction to Computer Science
Number Systems and Codes

## Slide 2: NUMBER SYSTEMS
Information Representation Review
Number Systems
Base Conversion
Negative Numbers
Floating-Point Number Representation
Decimal codes: BCD, Excess-3, 2421, 84-2-1
Alphanumeric Code
Error Detection

## Slide 3: INFORMATION REPRESENTATION REVIEW (1/3)
Numbers are important to computers
  Represent information precisely
  Can be processed
Examples
  Represent yes or no: use 0 and 1
  Represent the 4 seasons: 0, 1, 2 and 3
Sometimes, other characters are used
  Matriculation number: 8 alphanumeric characters (e.g.: U047004X)

## Slide 4: INFORMATION REPRESENTATION REVIEW (2/3)
Bit (Binary digit)
  0 and 1
  Represent false and true in logic
  Represent the on and off states in electronic devices
Other units
  Byte: 8 bits
  Nibble: 4 bits (seldom used)
  Word: Multiples of byte (e.g.: 1 byte, 2 bytes, 4 bytes, 8 bytes, etc.), depending on the architecture of the computer system

## Slide 5: INFORMATION REPRESENTATION REVIEW (3/3)
N bits can represent up to 2N values.
  Examples:
    2 bits  represent up to 4 values (00, 01, 10, 11)
    3 bits  represent up to 8 values (000, 001, 010, …, 110, 111)
    4 bits  represent up to 16 values (0000, 0001, 0010, …., 1111)
To represent M values, log2M bits are required.
  Examples:
    32 values  requires 5 bits
    64 values  requires 6 bits
    1024 values  requires 10 bits

## Slide 6: DECIMAL (BASE 10) SYSTEM (1/2)
A weighted-positional number system
  Base or radix is 10 (the base or radix of a number system is the total number of symbols / digits allowed in the system)
  Symbols / digit = { 0, 1, 2, 3, 4, 5, 6, 7, 8, 9 }
  Position is important, as the value of each symbol / digit is dependent on its type and its position in the number
  Example: The 9 in the two numbers below has different values:
    (7594)10 = (7 × 103) + (5 × 102) + (9 × 101) + (4 × 100)
    (912)10 = (9 × 102) + (1 × 101) + (2 × 100)
  In general,
(anan-1… a0 . f1f2 … fm)10 = (an x 10n) + (an-1x10n-1) + … + (a0 x 100) + (f1 x 10-1) + (f2 x 10-2) + … + (fm x 10-m)

## Slide 7: DECIMAL (BASE 10) SYSTEM (2/2)
Weighing factors (or weights) are in powers of 10:
  … 103 102 101 100 . 10-1 10-2 10-3 …
To evaluate the decimal number 593.68, the digit in each position is multiplied by the corresponding weight:
5102 + 9101 + 3100 + 610-1 + 810-2 = (593.68)10

## Slide 8: OTHER NUMBER SYSTEMS (1/2)
Binary (base 2)
  Weights in powers of 2
  Binary digits (bits): 0, 1
Octal (base 8)
  Weights in powers of 8
  Octal digits: 0, 1, 2, 3, 4, 5, 6, 7
Hexadecimal (base 16)
  Weights in powers of 16
  Hexadecimal digits: 0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F
Base R:
  Weights in powers of R

## Slide 9: OTHER NUMBER SYSTEMS (2/2)
In some programming languages, special notations are used to represent numbers in certain bases
  In programming language C
    Prefix 0x for hexadecimal.
    0x32 represents the hexadecimal number (32)16

## Slide 10: CONVERSION: BASE-R TO DECIMAL
Easy!
  1101.1012 = 123 + 122 + 120 + 12-1 + 12-3
  572.68 =
  2A.816 =
  341.245 =

## Slide 11: CONVERSION: DECIMAL TO BINARY
Method 1
  Sum-of-Weights Method
Method 2
  Repeated Division-by-2 Method, for whole numbers
  Repeated Multiplication-by-2 Method, for fractions

## Slide 12: SUM-OF-WEIGHTS METHOD
Determine the set of binary weights whose sum is equal to the decimal number
  (9)10 = 8 + 1 = 23 + 20 = (1001)2
  (18)10 = 16 + 2 = 24 + 21 = (10010)2
  (58)10 = 32 + 16 + 8 + 2 = 25 + 24 + 23 + 21 = (111010)2
  (0.625)10 = 0.5 + 0.125 = 2-1 + 2-3 = (0.101)2

## Slide 13: Repeated Multiplication-by-2 Method
To convert decimal fractions to binary,
  Use repeated multiplication, until the fractional product is 0 (or until the desired number of decimal places).
  The carried digits, or carries, produce the answer
    the first carry as the MSB
    the last as the LSB
  (0.3125)10 = (.0101)2
Suppose 0.3125 is multiplied by 2:
0.3125 is multiplier (or factor)
2 is multiplicand (or factor)
0.625 is product
625 is fractional product

## Slide 14: CONVERSION: DECIMAL AND OTHER BASES
Base-R to decimal: multiply digits with their corresponding weights.
Decimal to binary (base 2)
  Whole numbers repeated division-by-2
  Fractions: repeated multiplication-by-2
Decimal to base-R
  Whole numbers: repeated division-by-R
  Fractions: repeated multiplication-by-R

## Slide 15: CONVERSION BETWEEN BASES
In general, conversion between bases can be done via decimal:
Shortcuts for conversion between bases 2, 4, 8, 16
Base-2 Base-2
Base-3 Base-3
Base-4 Decimal Base-4
… ….
Base-R Base-R

## Slide 16: CONVERSION: BINARY TO OCTAL / HEXADECIMAL
Binary  Octal: partition in groups of 3
  (10 111 011 001 . 101 110)2 =
Octal  Binary: reverse
  (2731.56)8 =
Binary  Hexadecimal: partition in groups of 4
  (101 1101 1001 . 1011 1000)2 =
Hexadecimal  Binary: reverse
  (5D9.B8)16 =

## Slide 17: NEGATIVE NUMBERS
Unsigned numbers: only non-negative values.
Signed numbers: include all values (positive and negative)
  3 common representations for signed binary numbers:
    Sign-and-Magnitude
    1s Complement
    2s Complement
Notes: Computer does not recognize negative sign.

## Slide 18: SIGN-AND-MAGNITUDE (1/3)
The sign is represented by a ‘sign bit’
  0 for +
  1 for -
E.g.: a 1-bit sign and 7-bit magnitude format.
sign
magnitude
  00110100  +1101002 = ?
  10010011  -100112 = ?

## Slide 19: SIGN-AND-MAGNITUDE (2/3)
Largest value: 01111111 = +12710
Smallest value: 11111111 = -12710
Zeros: 00000000 = +010 10000000 = -010
Range: -12710 to +12710
Question:
  For an n-bit sign-and-magnitude representation, what is the range of values that can be represented?

## Slide 20: SIGN-AND-MAGNITUDE (3/3)
To negate a number, just invert the sign bit.
Examples:
  How to negate 00100001sm (decimal 33)? Answer: 10100001sm (decimal -33)
  How to negate 10000101sm (decimal -5)? Answer: 00000101sm (decimal +5)

## Slide 21: One’s COMPLEMENT (1/3)
Given a number x which can be expressed as an n-bit binary number, its negated value can be obtained in 1s-complement representation using:
-x = 2n – x – 1
Example: With an 8-bit number 00001100 (or 1210), its negated value expressed in 1s-complement is:
-000011002 = 28 – 12 – 1 (calculation in decimal) = 243 = 111100111s
(This means that -1210 is written as 11110011 in 1s-complement representation.)

## Slide 22: 1s COMPLEMENT (2/3)
Essential technique to negate a value: invert all the bits.
Largest value: 01111111 = +12710
Smallest value: 10000000 = -12710
Zeros: 00000000 = +010 11111111 = -010
Range: -12710 to +12710
The most significant (left-most) bit still represents the sign: 0 for positive; 1 for negative.

## Slide 23: 1s COMPLEMENT (3/3)
Examples (assuming 8-bit numbers):
(14)10 = (00001110)2 = (00001110)1s
-(14)10 = -(00001110)2 = (11110001)1s
-(80)10 = -( ? )2 = ( ? )1s

## Slide 24: 2s COMPLEMENT (1/3)
Given a number x which can be expressed as an n-bit binary number, its negated value can be obtained in 2s-complement representation using:
-x = 2n – x
Example: With an 8-bit number 00001100 (or 1210), its negated value expressed in 2s-complement is:
-000011002 = 28 – 12 (calculation in decimal) = 244 = 111101002s
(This means that -1210 is written as 11110100 in 2s-complement representation.)
Notes: This is commonly used. Arithmetic simpler.

## Slide 25: 2s COMPLEMENT (2/3)
Essential technique to negate a value: invert all the bits, then add 1.
Largest value: 01111111 = +12710
Smallest value: 10000000 = -12810
Zero: 00000000 = +010
Range: -12810 to +12710
The most significant (left-most) bit still represents the sign: 0 for positive; 1 for negative.

## Slide 26: 2s COMPLEMENT (3/3)
Examples (assuming 8-bit numbers):
(14)10 = (00001110)2 = (00001110)2s
-(14)10 = -(00001110)2 = (11110010)2s
-(80)10 = -( ? )2 = ( ? )2s
Comparison:
(14)10 = (00001110)2 = (00001110)1s
-(14)10 = -(00001110)2 = (11110001)1s

## Slide 27: COMPARISON
4-bit system
Positive values Negative values

## Slide 28: COMPLEMENT ON FRACTIONS
We can extend the idea of complement on fractions.
Examples:
  Negate 0101.01 in 1s-complement Answer: 1010.10
  Negate 111000.101 in 1s-complement Answer: 000111.010
  Negate 0101.01 in 2s-complement Answer: 1010.11

## Slide 29: 1s COMPLEMENT: ADDITION/SUBTRACTION (1/2)
Algorithm for addition, A + B:
  Perform binary addition on the two numbers.
  If there is a carry out of the MSB, add 1 to the result.
  Check for overflow. Overflow occurs if result is opposite sign of A and B.
Algorithm for subtraction, A – B: A – B = A + (-B)
  Take 1s-complement of B.
  Add the 1s-complement of B to A.

## Slide 30: 1s COMPLEMENT: ADDITION/SUBTRACTION (2/2)
Examples: 4-bit system
+3 0011
+ +4 + 0100
---- -------
+7 0111
---- -------
+5 0101
+ -5 + 1010
---- -------
-0 1111
---- -------
-2 1101
+ -5 + 1010
---- ------
-7 10111
---- + 1
------
1000
-3 1100
+ -7 + 1000
---- -------
-10 10100
---- + 1
-------
0101
Any overflow?
Notes: Right low

## Slide 31: 2s COMPLEMENT: ADDITION/SUBTRACTION (1/3)
Algorithm for addition, A + B
  Perform binary addition on the two numbers.
  Ignore the carry out of the MSB.
  Check for overflow. Overflow occurs if the ‘carry in’ and ‘carry out’ of the MSB are different, or if result is opposite sign of A and B.
Algorithm for subtraction, A – B A – B = A + (-B)
  Take 2s-complement of B.
  Add the 2s-complement of B to A.

## Slide 32: OVERFLOW
Signed numbers are of a fixed range.
If the result of addition/subtraction goes beyond this range, an overflow occurs.
Overflow can be easily detected:
  positive add positive  negative
  negative add negative  positive
Example: 4-bit 2s-complement system
  Range of value: -810 to 710
  01012s + 01102s = 10112s 510 + 610 = -510 ?! (overflow!)
  10012s + 11012s = 101102s (discard end-carry) = 01102s -710 + -310 = 610 ?! (overflow!)

## Slide 33: 2s COMPLEMENT: ADDITION/SUBTRACTION (2/3)
Examples: 4-bit system
Which of the above is/are overflow(s)?
+3 0011
+ +4 + 0100
---- -------
+7 0111
---- -------
-2 1110
+ -6 + 1010
---- -------
-8 11000
---- -------
+6 0110
+ -3 + 1101
---- -------
+3 10011
---- -------
+4 0100
+ -7 + 1001
---- -------
-3 1101
---- -------
Notes: No overflow

## Slide 34: 2s COMPLEMENT: ADDITION/SUBTRACTION (3/3)
Examples: 4-bit system
Which of the above is/are overflow(s)?
-3 1101
+ -6 + 1010
---- -------
-9 10111
---- -------
+5 0101
+ +6 + 0110
---- -------
+11 1011
---- -------
Notes: Both overflow.

## Slide 35: FIXED POINT NUMBERS (1/2)
In fixed point representation, the binary point is assumed to be at a fixed location.
  For example, if the binary point is at the end of an 8-bit representation as shown below, it can represent integers from -128 to +127.
binary point

## Slide 36: FIXED POINT NUMBERS (2/2)
In general, the binary point may be assumed to be at any pre-fixed location.
  Example: Two fractional bits are assumed as shown below.
  If 2s complement is used, we can represent values like:
  011010.112s = 26.7510
  111110.112s = -000001.012 = -1.2510
assumed binary point
integer part
fraction part

## Slide 37: FLOATING POINT NUMBERS (1/4)
Fixed point numbers have limited range.
Floating point numbers allow us to represent very large or very small numbers.
Examples: 0.23 × 1023 (very large positive number) 0.5 × 10-37 (very small positive number) -0.2397 × 10-18 (very small negative number)

## Slide 38: FLOATING POINT NUMBERS (2/4)
3 parts: sign, mantissa, and exponent
The base (radix) is assumed to be 2.
Sign bit: 0 for positive, 1 for negative.
sign
mantissa
exponent
Mantissa is usually in normalized form (the integer part is zero and the fraction part must not begin with zero)
  0.01101 × 24  normalised  0.1101 x 23
  101011.0110 × 2-4  normalised 
Trade-off:
  More bits in mantissa  better precision
  More bits in exponent  larger range of values
Notes: 0.01101 x 2^4 = 0.1101 x 2^3

## Slide 39: FLOATING POINT NUMBERS (3/4)
Exponent is usually expressed in complement or excess format.
Example: Express -6.510 in base-2 normalized form -6.510 = -110.12 = -0.11012 × 23
Assuming that the floating-point representation contains 1-bit, 5-bit normalised mantissa, and 4-bit exponent. The above example will be stored as if the exponent is in 1s or 2s complement.
1
11010
0011

## Slide 40: FLOATING POINT NUMBERS (4/4)
Example: Express 0.187510 in base-2 normalised form
  0.187510 = 0.00112 = 0.11 × 2-2
Assume this floating-point representation:1-bit sign, 5-bit normalised mantissa, and 4-bit exponent.
The above example will be represented as
0
11000
1101
If exponent is in 1’s complement.
0
11000
1110
If exponent is in 2’s complement.

## Slide 41: DECIMAL CODES
Decimal numbers are favoured by humans. Binary numbers are natural to computers. Hence, conversion is required.
If little calculation is required, we can use some coding schemes to store decimal numbers, for data transmission purposes.
Examples: BCD
Each decimal digit is represented as a 4-bit code.
The number of digits in a code is also called the length of the code.
Notes: How to translate

## Slide 42: BINARY CODE DECIMAL (BCD) (1/2)
Some codes are unused, like 1010BCD, 1011BCD, … 1111BCD. These codes are considered as errors.
Easy to convert, but arithmetic operations are more complicated.
Suitable for interfaces such as keypad inputs.
Decimal digit | BCD
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1001
Notes: How to translate

## Slide 43: BINARY CODE DECIMAL (BCD) (2/2)
Examples of conversion between BCD values and decimal values:
  (234)10 = (0010 0011 0100)BCD
  (7093)10 = (0111 0000 1001 0011)BCD
  (1000 0110)BCD = (86)10
  (1001 0100 0111 0010)BCD = (9472)10
Note that BCD is not equivalent to binary
  Example: (234)10 = (11101010)2
Notes: How to translate

## Slide 44: ALPHA-NUMERIC CODES (1/3)
Computers also handle textual data.
Character set frequently used:
  alphabets: ‘A’ … ‘Z’, ‘a’ … ‘z’
  digits: ‘0’ … ‘9’
  special symbols: ‘$’, ‘.’, ‘@’, ‘*’, etc.
  non-printable: NULL, BELL, CR, etc.
Examples
  ASCII (8 bits), Unicode
Notes: We want to use text

## Slide 45: ALPHA-NUMERIC CODES (2/3)
ASCII
  American Standard Code for Information Interchange
  7 bits, plus a parity bit for error detection
  Odd or even parity
Notes: We want to use text

## Slide 46: ALPHA-NUMERIC CODES (3/3)
ASCII table
A: 1000001