## Slide 1: Introduction to Computer Science
Boolean Algebra

## Slide 2: BOOLEAN ALGEBRA
Boolean Algebra
Precedence of Operators
Truth Table
Duality
Basic Theorems
Complement of Functions
Standard Forms
Minterms and Maxterms
Canonical Forms

## Slide 3: DIGITAL CIRCUITS (1/2)
Two voltage levels
  High, true, 1, asserted
  Low, false, 0, de-asserted
Signals in digital circuit
High
Low
Signals in analog circuit
A digital watch

## Slide 4: DIGITAL CIRCUITS (2/2)
Advantages of digital circuits over analog circuits
  More reliable (simpler circuits, less noise-prone)
  Specified accuracy (determinable)
  Abstraction can be applied using simple mathematical model – Boolean Algebra
  Ease design, analysis and simplification of digital circuit – Digital Logic Design
Notes: Logical vs. physical

## Slide 5: TYPES OF LOGIC BLOCKS
Combinational: no memory, output depends solely on the input
  Gates
  Decoders, multiplexers
  Adders, multipliers
Sequential: with memory, output depends on both input and current state.
  Counters, registers
  Memories

## Slide 6: BOOLEAN ALGEBRA
Boolean values:
  True (1)
  False (0)
Connectives
  Conjunction (AND)
    A  B; A  B
  Disjunction (OR)
    A + B; A  B
  Negation (NOT)
    Ā /A’
Truth tables
A | B | A  B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | B | A + B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | Ā
0 | 1
1 | 0
Logic gates
A
B
AB
A
B
A+B
A
Ā

## Slide 7: LAWS OF BOOLEAN ALGEBRA
Identity laws
  A + 0 = 0 + A = A ; A  1 = 1  A = A
Inverse/complement laws
  A + Ā = 1 ; A  Ā = 0
Commutative laws
  A + B = B + A ; A  B = B  A
Associative laws
  A + (B + C) = (A + B) + C ; A  (B  C) = (A  B)  C
Distributive laws
  A  (B + C) = (A  B) + (A  C) ; A + (B  C) = (A + B)  (A + C)
Notes: A + (B  C) = (A+B)  (A+C) less straightforward

## Slide 8: PRECEDENCE OF OPERATORS
Precedence from highest to lowest
  Not
  And
  Or
Examples:
  A  B + C = (A  B) + C
  B + Ā = B + (Ā)
  P + Q'  R = P + ((Q')  R)
Use parenthesis to overwrite precedence. Examples:
  A  (B + C)
  (P + Q)'  R

## Slide 9: TRUTH TABLE
Provide a listing of every possible combination of inputs and its corresponding outputs.
  Inputs are usually listed in binary sequence.
Example
  Truth table with 3 inputs and 2 outputs
x | y | z | y + z | x  (y + z)
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1

## Slide 10: PROOF USING TRUTH TABLE
Prove: x  (y + z) = (x  y) + (x  z)
  Construct truth table for LHS and RHS
  Check that column for LHS = column for RHS
x | y | z | y + z | x  (y + z) | x  y | x  z | (x  y) + (x  z)
0 | 0 | 0 |  |  |  |  | 
0 | 0 | 1 |  |  |  |  | 
0 | 1 | 0 |  |  |  |  | 
0 | 1 | 1 |  |  |  |  | 
1 | 0 | 0 |  |  |  |  | 
1 | 0 | 1 |  |  |  |  | 
1 | 1 | 0 |  |  |  |  | 
1 | 1 | 1 |  |  |  |  | 

## Slide 11: DUALITY
If the AND/OR operators and identity elements 0/1 in a Boolean equation are interchanged, it remains valid
Example:
  The dual equation of a+(bc)=(a+b)(a+c) is a(b+c)=(ab)+(ac)
Duality gives free theorems – “two for the price of one”. You prove one theorem and the other comes for free!
Examples:
  If (x+y+z)' = x'y'z' is valid, then its dual is also valid: (xyz)' = x'+y'+z'
  If x+1 = 1 is valid, then its dual is also valid: x0 = 0
Note: It does not mean (x+y+z)' and (xyz)' are the same

## Slide 12: BASIC THEOREMS (1/2)
Idempotency
  X + X = X ; X  X = X
Zero and One elements
  X + 1 = 1 ; X  0 = 0
Involution
  ( X' )' = X
Absorption
  X + XY = X ; X(X + Y) = X
Absorption (variant)
  X + X'Y = X + Y ; X(X' + Y) = XY
Notes: X + X'Y = X + Y is not intuitive. But it is useful

## Slide 13: BASIC THEOREMS (2/2)
DeMorgan’s
  (X + Y)' = X'  Y' ; (X  Y)' = X' + Y'
DeMorgan’s Theorem can be generalized to more than two variables, example: (A + B + … + Z)' = A'  B'  …  Z'
Consensus
  XY + X'Z + YZ = XY + X'Z (X+Y)(X'+Z)(Y+Z) = (X+Y)(X'+Z)
Notes: Consensus not intuitive

## Slide 14: PROVING A THEOREM
Theorems can be proved using truth table, or by algebraic manipulation using other theorems/laws.
Example: Prove absorption theorem X + XY = X
  X + XY = X1 + XY (identity)
  = X(1+Y) (distributivity) = X(Y+1) (commutativity)
  = X1 (one element) = X (identity)
  By duality, we have also proved X(X+Y) = X

## Slide 15: COMPLEMENT
Given a Boolean function F, the complement of F, denoted as F', is obtained by interchanging 1 with 0 in the function’s output values.
Example: F1 = xyz'
What is F1' ?
x | y | z | F1 | F1'
0 | 0 | 0 | 0 | 
0 | 0 | 1 | 0 | 
0 | 1 | 0 | 0 | 
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | 0 | 

## Slide 16: BOOLEAN ALGEBRA
Boolean Algebra
Precedence of Operators
Truth Table
Duality
Basic Theorems
Complement of Functions
Standard Forms
Minterms and Maxterms
Canonical Forms

## Slide 17: STANDARD FORMS (1/2)
Certain types of Boolean expressions lead to circuits that are desirable (from implementation viewpoint).
Two standard forms:
  Sum-of-Products
  Product-of-Sums
Literals
  A Boolean variable on its own or in its complemented form
  Examples: x, x', y, y'
Product term
  A single literal or a logical product (AND) of several literals
  Examples: x, xyz', A'B, AB, dg'vw
Notes: Why learn this?

## Slide 18: STANDARD FORMS (2/2)
Sum term
  A single literal or a logical sum (OR) of several literals
  Examples: x, x+y+z', A'+B, A+B, c+d+h'+j
Sum-of-Products (SOP) expression
  A product term or a logical sum (OR) of several product terms
  Examples: x, x + yz', xy' + x'yz, AB + A'B', A + B'C + AC' + CD
Product-of-Sums (POS) expression
  A sum term or a logical product (AND) of several sum terms
  Examples: x, x(y+z'), (x+y')(x'+y+z), (A+B)(A'+B'), (A+B+C)D'(B'+D+E')
Every Boolean expression can be expressed in SOP or POS.

## Slide 19: DO IT YOURSELF
SOP : A product term or a logical sum (OR) of several product terms.
POS : A sum term or a logical product (AND) of several sum terms.
Put the right ticks in the following table.
Expression | SOP? | POS?
X'∙Y + X∙Y' + X∙Y∙Z |  | 
(X+Y')∙(X'+Y)∙(X'+Z') |  | 
X' + Y + Z |  | 
X∙Y∙Z' |  | 
W∙X'∙Y + V∙(X∙Z + W') |  | 

## Slide 20: MINTERMS & MAXTERMS (1/2)
A minterm of n variables is a product term that contains n literals from all variables.
  Example: Given 2 variables x and y, the minterms are:
  x'∙y', x'∙y, x∙y' and x∙y
A maxterm of n variables is a sum term that contains n literals from all variables.
  Example: Given 2 variables x and y, the maxterms are:
  x'+y', x'+y, x+y' and x+y
In general, given n variables, we have 2n minterms and 2n maxterms.

## Slide 21: MINTERMS & MAXTERMS (2/2)
The minterms and maxterms on 2 variables are denoted by m0 to m3 and M0 to M3, respectively.
x | y | Minterms |  | Maxterms | 
 |  | Term | Notation | Term | Notation
0 | 0 | x'∙y' | m0 | x+y | M0
0 | 1 | x'∙y | m1 | x+y' | M1
1 | 0 | x∙y' | m2 | x'+y | M2
1 | 1 | x∙y | m3 | x'+y' | M3
A minterm is the complement of the corresponding maxterm
  Example: m2 = x∙y' m2' = ( x∙y' )' = x' + ( y' )' = x' + y = M2

## Slide 22: CANONICAL FORMS
Canonical (or normal) form: a unique form of representation.
  Sum-of-minterms = Canonical sum-of-products
  Product-of-maxterms = Canonical product-of-sums

## Slide 23: SUM-OF-MINTERMS
Given a truth table:
x | y | z | F1 | F2 | F3
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 1 | 0
1 | 1 | 1 | 0 | 1 | 0
Obtain sum-of-minterms expression by gathering the minterms of the function (where output is 1).
F1 = x∙y∙z' = m6
F2 =
F3 =

## Slide 24: PRODUCT-OF-MAXTERMS
Given a truth table:
x | y | z | F1 | F2 | F3
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 1 | 0
1 | 1 | 1 | 0 | 1 | 0
Obtain product-of-maxterms expression by gathering the maxterms of the function (where output is 0).
F2 = (x+y+z) ∙ (x+y'+z) ∙ (x+y'+z') = M0 ∙ M2 ∙ M3 = PM(0,2,3)
F3 =

## Slide 25: CONVERSION
We can convert between sum-of-minterms and product-of-maxterms
Example: F2 = S m(1,4,5,6,7) = P M(0,2,3)
Why? See F2' in truth table.
  F2' = m0 + m2 + m3
  Therefore, F2 = (m0 + m2 + m3)' = m0' ∙ m2' ∙ m3' (by DeMorgan’s) = M0 ∙ M2 ∙ M3 (mx' = Mx)
x | y | z | F2 | F2'
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0

## Slide 26: KARNAUGH MAPS
Function Simplification
  Algebraic Simplification
Introduction to K-maps
How to use K-maps
Converting to Minterms Form
Example on Finding Minimal SOP Expression
Finding POS Expression
Don’t-care Conditions

## Slide 27: FUNCTION SIMPLIFICATION
Why simplify?
  Simpler expression uses fewer logic gates.
  Thus cheaper, uses less power, (sometimes) faster.
Techniques
  Algebraic
    Using theorems
    Open-ended; requires skills
  Karnaugh Maps
    Easy to use
    Limited to no more than 6 variables
  Quine-McCluskey (not going to cover)
    Suitable for automation
    Can handle many variables (but computationally intensive)

## Slide 28: ALGEBRAIC SIMPLIFICATION (1/4)
Aims to minimize
  Number of literals, and
  Number of terms
But sometimes conflicting, so let’s aim at reducing the number of literals for the examples in the next few slides.
Difficult – needs good algebraic manipulation skills.

## Slide 29: ALGEBRAIC SIMPLIFICATION (2/4)
Example 1: Simplify (x+y)(x+y')(x'+z)
  (x+y)(x+y')(x'+z) = (xx + xy' + xy + yy')  (x'+z) (distributivity) = (x + x(y'+y) + 0)  (x'+z) (idemp, assoc., complement) = (x + x1)  (x'+z) (complement, identity) = (x + x)  (x'+z) (identity) = x  (x'+z) (idempotency) = xx' + xz (distributivity) = 0 + xz (complement) = xz (identity)
Number of literals reduced from 6 to 2.

## Slide 30: ALGEBRAIC SIMPLIFICATION (3/4)
Example 2: Find simplified SOP and POS expressions of F(x,y,z) = x'y(z+y'x) + y'z
  =
Simplified SOP:
Simplified POS:
Notes: SOP: x’  y  z + x’  y  y’  x + y’  z = x’  y  z + y’  z (Check)
POS: Z  (X’  Y + Y’) = Z  (X’ + Y’) [Absorption]

## Slide 31: ALGEBRAIC SIMPLIFICATION (4/4)
Example 3: Find minimal SOP expression of F(a,b,c,d) = abc + abd + a'bc' + cd + bd'
  = abc + abd + a'bc' + cd + bd' =
Notes: a*b*d + b * d’ = b*(ad+d’) = b*(a + d’) = ab + bd’ (absorption)
a + a’ c’ = a + c’ (absoption)
a*b + a’ * b * c’ + c * d + b * d’ = b (a + a’ c’ ) + c * d + b * d’ = b (a + c’) + c * d + b * d’ = a * b + b * c’ + c * d + b * d’

## Slide 32: INTRODUCTION TO K-MAPS
Systematic method to obtain simplified (minimal) sum-of-products (SOP) expressions.
Objective:
  Fewest possible product terms and literals.
Diagrammatic technique based on a special form of Venn diagram.
  Advantage: Easy to use.
  Disadvantage: Limited (to 5 or 6) variables.

## Slide 33: VENN DIAGRAM
Example:
  2 variables a and b represented by 2 circular regions.
  There are 4 minterms, each occupying their respective space.
ab'
a'b
a'b'
ab
a
b
A set of minterms represents a certain Boolean function.
Examples:
  { a∙b, a∙b' }  a∙b + a∙b' = a∙(b+b') = a
  { a'∙b, a∙b }  a'∙b + a∙b = (a'+a)∙b = b
  { a∙b }  a∙b
  { a∙b, a∙b', a'∙b }  a∙b + a∙b' + a'∙b = a + b
  { }  0
  { a'∙b', a∙b, a∙b', a'∙b }  1

## Slide 34: 2-VARIABLE K-MAPS (1/2)
Karnaugh-map (K-map) is an abstract form of Venn diagram, organised as a matrix of squares, where
  Each square represents a minterm
  Two adjacent squares represent minterms that differ by exactly one literal
Given 2 variables a and b, K-map can be drawn as…
a'b'
a'b
ab'
ab
a
b
m0
m1
m2
m3
a
b
a
b
0 1
0
1

## Slide 35: 3-VARIABLE K-MAPS (1/2)
There are 8 minterms for 3 variables.
There are 8 squares in a K-map.
Example: Let the variables be a, b, c.
ab'c'
ab'c
a
b
abc
abc'
a'b'c'
a'b'c
a'bc
a'bc'
0
1
00 01 11 10
c
a
bc
m4
m5
a
b
m7
m6
m0
m1
m3
m2
c
a
bc
0
1
00 01 11 10
Gray code sequence
Above arrangement ensures that minterms of adjacent cells differ by only ONE literal.
Other arrangements which satisfy this criterion may also be used.

## Slide 36: 3-VARIABLE K-MAPS (2/2)
There is wrap-around in the K-map:
  a'∙b'∙c' (m0) is adjacent to a'∙b∙c' (m2)
  a∙b'∙c' (m4) is adjacent to a∙b∙c' (m6)
m4
m5
m7
m6
m0
m1
m3
m2
0
1
00 01 11 10
a
bc
Each cell in a 3-variable K-map has 3 adjacent neighbours.
In general, each cell in an n-variable K-map has n adjacent neighbours.
For example, m0 has 3 adjacent neighbours: m1, m2 and m4.

## Slide 37: QUICK REVIEW QUESTIONS (1)
5-1.The K-map of a 3-variable function F is shown below. What is the sum-of-minterms expression of F?
5-2. Draw the K-map for this function A:
A(x, y, z) = x∙y + y∙z' + x'∙y'∙z
0
1
a
b
0
0
1
0
0
1
0
1
00 01 11 10
c
a
bc

## Slide 38: 4-VARIABLE K-MAPS (1/2)
There are 16 square cells in a 4-variable K-map.
Example: Let the variables be w, x, y, z.
m4
m5
w
y
m7
m6
m0
m1
m3
m2
00
01
11
10
00 01 11 10
z
wx
yz
m12
m13
m15
m14
m8
m9
m11
m10
x

## Slide 39: 4-VARIABLE K-MAPS (2/2)
There are 2 wrap-arounds.
Every cell has 4 neighbours.
  Example:
    The cell corresponding to minterm m0 has neighbours m1, m2, m4 and m8.
m4
m5
w
y
m7
m6
m0
m1
m3
m2
z
wx
yz
m12
m13
m15
m14
m8
m9
m11
m10
x

## Slide 40: HOW TO USE K-MAPS (1/7)
Based on the Unifying Theorem (complement law):
  A + A' = 1
In a K-map, each cell containing a ‘1’ corresponds to a minterm of a given function F.
Each valid grouping of adjacent cells containing ‘1’ then corresponds to a simpler product term of F.
  A group must have size in powers of two: 1, 2, 4, 8, …
    Grouping 2 adjacent cells eliminates 1 variable from the product term.
    Grouping 4 cells eliminates 2 variables.
    Grouping 8 cells eliminates 3 variables.
    In general, grouping 2n cells eliminates n variables.

## Slide 41: HOW TO USE K-MAPS (2/7)
Group as many cells as possible
  The larger the group, the fewer the number of literals in the resulting product term.
Select as few groups as possible to cover all the cells (minterms) of the function
  The fewer the groups, the fewer is the number of product terms in the simplified (minimal) SOP expression.

## Slide 42: HOW TO USE K-MAPS (3/7)
Example:
F (w,x,y,z) = w'∙x∙y'∙z' + w'∙x∙y'∙z + w∙x'∙y∙z'
+ w∙x'∙y∙z + w∙x∙y∙z' + w∙x∙y∙z
=  m(4, 5, 10, 11, 14, 15)
1
1
w
y
00
01
11
10
00 01 11 10
wx
yz
1
1
1
1
x
(cells with ‘0’ are not
shown for clarity)

## Slide 43: HOW TO USE K-MAPS (4/7)
Each group of adjacent minterms corresponds to a possible product term of the given function.
Here, there are 2 groups of minterms, A and B:
  A = w'.x.y'.z' + w'.x.y'.z = w'.x.y'.(z' + z) = w'.x.y'
  B = w.x'.y.z' + w.x'.y.z + w.x.y.z' + w.x.y.z
  = w.x'.y.(z' + z) + w.x.y.(z' + z)
  = w.x'.y + w.x.y
  = w.(x'+x).y
  = w.y
1
1
w
00
01
11
10
00 01 11 10
z
wx
yz
1
1
1
1
x
A
B
y

## Slide 44: HOW TO USE K-MAPS (5/7)
Each product term that corresponds to a group, w'∙x∙y' and w∙y, represents the sum of minterms in that group.
Boolean expression is therefore the sum of product terms (SOP) that represent all groups of the minterms of the function:
  F(w,x,y,z) = group A + group B = w'∙x∙y' + w∙y

## Slide 45: HOW TO USE K-MAPS (6/7)
The larger the group (the more minterms it contains), the fewer is the number of literals in the associated product term.
  Recall that a group must have size in powers of two.
  Example: For a 4-variable K-map with variables w, x, y, z 1 cell = 4 literals. Examples: w∙x∙y∙z, w'∙x∙y'∙z 2 cells = 3 literals. Examples: w∙x∙y, w∙y'∙z' 4 cells = 2 literals. Examples: w∙x, x'∙y 8 cells = 1 literal. Examples: w, y', z 16 cells = no literal (i.e. logical constant 1). Example: 1

## Slide 46: HOW TO USE K-MAPS (7/7)
Examples of valid and invalid groupings.
1
1
1
1
1
1
1
1
P
1
1
1
1
1
1
1
1
P
P
1
1
1
1
1
1
1
1
1
1
1
1
1
1
O
1
1
1
1
1
1
O

## Slide 47: CONVERTING TO MINTERMS FORM (1/2)
The K-map of a function can be easily filled in when the function is given in sum-of-minterms form.
What if it is not in sum-of-minterms form?
  Convert it into sum-of-products (SOP) form
  Expand the SOP expression into sum-of-minterms expression, or fill in the K-map directly based on the SOP expression.

## Slide 48: CONVERTING TO MINTERMS FORM (2/2)
Example:
  F(A,B,C,D) = A.(C+D)'.(B'+D') + C.(B+C'+A'.D) = A.(C'.D').(B'+D') + B.C + C.C' + A'.C.D = A.B'.C'.D' + A.C'.D' + B.C + A'.C.D
1
1
C
A
00
01
11
10
00 01 11 10
B
CD
AB
D
1
1
1
1
1
A.B'.C'.D' + A.C'.D' + B.C + A'.C.D
= A.B'.C'.D' + A.C'.D'.(B+B') + B.C + A'.C.D
= A.B'.C'.D' + A.B.C'.D' + A.B'.C'.D' + B.C.(A+A') + A'.C.D
= A.B'.C'.D' + A.B.C'.D' + A.B.C + A'.B.C + A'.C.D
= A.B'.C'.D' + A.B.C'.D' + A.B.C.(D+D') + A'.B.C.(D+D') + A'.C.D.(B+B')
= A.B'.C'.D' + A.B.C'.D' + A.B.C.D + A.B.C.D' + A'.B.C.D + A'.B.C.D' + A'.B‘.C.D

## Slide 49: Appendix