## Slide 1: Introduction to Computer Science
Computer Networks

## Slide 2: Objectives
In this chapter, you will learn about
Basic networking concepts
Communication protocols
Network services and benefits
A brief history of the Internet and the World Wide Web

## Slide 3: Basic Networking Concepts
Computer network
  Set of independent computer systems connected by telecommunication links
  Purpose: Sharing information and resources
Nodes, hosts, or end systems
  Individual computers on a network

## Slide 4: Communication Links
Switched, dial-up telephone line
  A circuit is temporarily established between the caller and callee
  Analog medium
  Requires modem at both ends to transmit information produced by a computer
    Computer produces digital information
Two Forms of Information Representation

## Slide 5
Modulation of a Carrier to Encode Binary Information

## Slide 6: Communication Links (continued)
Dial-up phone links
  Transmission rate: 56,000 bps (56 Kbps)
Broadband
  Transmission rate: Exceeding 256,000 bps (256 Kbps)

## Slide 7: Communication Links (continued)
Broadband communications
  Home use
    Digital subscriber line (DSL)
    Cable modem
  Commercial and office environment
    Ethernet
    Fast Ethernet
    Gigabit Ethernet

## Slide 8: Communication Links (Home use)
USB/Ethernet Cable
DSL/Cable Modem
Wall Jack
Ethernet Cable
DSL/Cable Modem
Wall Jack
Hub/Switch/Router
Single machine
Multiple machines

## Slide 9: Communication Links (Home use)
Ethernet Cable
DSL/Cable Modem
Wall Jack
Hub/Switch/Router
Home wireless network

## Slide 10
Transmission Time of an Image at Different Transmission Speeds

## Slide 11: Communication Links (continued)
Wireless data communication
  Uses radio, microwave, and infrared signals
  Enables “mobile computing”
  Types of wireless data communication
    Wireless local access network
    Wireless wide-area access network

## Slide 12: Network Types
LAN
WLAN
WAN

## Slide 13: Local Area Networks
A network of computers that are in the same physical location, such as home or building
Common wired LAN topologies
  Bus
  Ring
  Star

## Slide 14
An Ethernet LAN Implemented Using Shared Cables

## Slide 15
An Ethernet LAN Implemented Using a Hub

## Slide 16: Local Area Networks (continued)
Ethernet
  Most widely used LAN technology
  Uses the bus topology
  Two ways to construct an Ethernet LAN
    Shared cable
    Hubs: The most widely used technology

## Slide 17: LAN (Local Area Network)
Ethernet Standard
  10BaseT
    10Mbps (Mega bits per second)
  100BaseT
    100Mbps
  1000BaseT
    1000Mbps or 1Gbps

## Slide 18: LAN (Local Area Network)
http://en.wikipedia.org/wiki/Image:Ethernet_RJ45_connector_p1160054.jpg
http://en.wikipedia.org/wiki/Image:BNC_connector.jpg
Old: BNC connector for coaxial cable
New: RJ45 for twisted pair cable

## Slide 19: LAN (Local Area Network)
Question: Can 2 computers communicate by connecting each other using an Ethernet cable back-to-back?

## Slide 20: WLAN (Wireless LAN)
Wi-Fi (Wireless Fidelity)
  A wireless technology that connects computers without cables
Access Point (AP)
  A device (base station) that connects wireless devices together
  Usually connected to a wired-network
ESSID (Extended Service Set ID)
  A “name” for the AP, eg. mobilenet
Hotspot
  The area covered by wireless access points

## Slide 21: WLAN (Wireless LAN)
Standard
  802.11b - 11Mbps
  802.11g - 54Mbps
  802.11a - 54Mbps
Security
  WEP (Wired Equivalen Privacy)
  WPA (Wi-Fi Protected Access)
  To prevent wardriving
2.4G
5G

## Slide 22: Wide Area Networks
Wide area networks (WANs)
  Connect devices that are across town, across the country, or across the ocean
  Users must purchase telecommunications services from an external provider
  Dedicated point-to-point lines
Typical Structure of a Wide Area Network

## Slide 23: Overall Structure of the Internet
All real-world networks, including the Internet, are a mix of LANs and WANs
  Example: A company or a college
    One or more LANs connecting its local computers
    Individual LANs interconnected into a wide-area company network

## Slide 24
Structure of a Typical Company Network

## Slide 25: Overall Structure of the Internet (continued)
Internet Service Provider (ISP)
  A wide-area network
  Provides a pathway from a specific network to other networks, or from an individual’s computer to other networks
ISPs are hierarchical
  Interconnect to each other in multiple layers to provide greater geographical coverage

## Slide 26
Structure of a Network Using an ISP

## Slide 27
Hierarchy of Internet Service Providers

## Slide 28: Overall Structure of the Internet (continued)
Internet
  A huge interconnected “network of networks”
  Includes nodes, LANs, WANs, bridges, routers, and multiple levels of ISPs
  Early 2005
    317 million nodes (hosts)
    Hundreds of thousands of separate networks located in over 225 countries
Notes: Click will bring up the statistics from 2003

## Slide 29: Communication Protocols
A protocol
  A mutually agreed upon set of rules, conventions, and agreements for the efficient and orderly exchange of information
TCP/IP
  The Internet protocol hierarchy
  Governs the operation of the Internet
  Five layers

## Slide 30: TCP/IP
The Five-Layer TCP/IP Internet Protocol Hierarchy
Segments
Packets
Frames
Bits
Data

## Slide 31: Packets
A small chunk of data transmitted over the Internet
Alice
The Internet
Bob

## Slide 32: Physical Layer
Protocols govern the exchange of binary digits across a physical communication channel
Goal: Create a bit pipe between two network devices Details: voltage levels, wavelengths, radio frequencies Note: different specifications for different machines and different mode of communication

## Slide 33: Data Link Layer
Protocols carry out
  Error handling (detection and correction)
  Framing - identify the start and stop of a message
Creates an error-free message pipe
Composed of two services
  Layer 2a: Medium access control
  Layer 2b: Logical link control

## Slide 34: Network Layer (IP protocol)
Delivers a message from the site where it was created to its ultimate destination
Critical responsibilities
  Create a universal addressing scheme for all network nodes
  Deliver messages between any two nodes in the network (route the packets between two nodes)

## Slide 35: Network Layer (continued)
Provides a true network delivery service
  Messages are delivered between any two nodes in the network, regardless of where they are located
IP (Internet Protocol) layer
  Network layer in the Internet

## Slide 36: Network Layer (continued)
Router
Router
Key concepts
Host names
example: gordon.edu
IP addresses
example: 200.56.34.100
Domain name system (DNS)
(def) converts a symbolic host name to 32-bit IP address
Routing
store and forward & best path

## Slide 37: Transport Layer
Provides a high-quality, error-free, order- preserving, end-to-end delivery service
TCP (Transport Control Protocol)
  Primary transport protocol on the Internet
  Requires the source and destination programs to initially establish a connection

## Slide 38: Transport Layer
Router
Router
Host A: 122.45.65.17
Host B: 100.44.44.5
Port: 23
Port: 78
Port: 80
Port: 567
Key Concepts
1. Port Numbers
(def) identifies a specific application on a host
2. Well-known port numbers
3. TCP (transport control protocol)
requires a handshake and connection setup
4. UDP (user datagram protocol)

## Slide 39
Logical View of a TCP Connection

## Slide 40: Application Layer
Implements the end-user services provided by a network
There are many application protocols
  HTTP (hypertext transfer protocol)
  SMTP (simple mail transfer protocol)
  POP3
  IMAP
  FTP (file transfer protocol)

## Slide 41
Some Popular Application Protocols on the Internet

## Slide 42: Application Layer (continued)
Uniform Resource Locator (URL)
  A symbolic string that identifies a Web page
  Form
    protocol://host address/page
  The most common Web page format is hypertext information
    Accessed using the HTTP protocol

## Slide 43: Network Services and Benefits
Services offered by computer networks
  Electronic mail (email)
  Bulletin boards
  News groups
  Chat rooms
  Resource sharing
    Physical resources
    Logical resources

## Slide 44: Network Services and Benefits (continued)
Services offered by computer networks
  Client-server computing
  Information sharing
  Information utility
  Electronic commerce (e-commerce)

## Slide 45: A Brief History of the Internet and the World Wide Web: The Internet
August 1962: First proposal for building a computer network
  Made by J. C. R. Licklider of MIT
ARPANET
  Built by the Advanced Research Projects Agency (ARPA) in the 1960s
  Grew quickly during the early 1970s

## Slide 46: The Internet (continued)
NSFNet: A national network built by the National Science Foundation (NSF)
October 24, 1995: Formal acceptance of the term Internet
Internet service providers start offering Internet access once provided by the ARPANET and NSFNet

## Slide 47
State of Networking in the Late 1980s

## Slide 48: The World Wide Web
Development completed in May 1991
Designed and built by Tim Berners-Lee
Components
  Hypertext
    A collection of documents interconnected by pointers called links
  URL (Uniform Resource Locator)
    The worldwide identification of a Web page located on a specific host computer

## Slide 49
Hypertext Documents

## Slide 50: Summary
Computer network: A set of independent computer systems connected by telecommunication links
Options for transmitting data on a network: Dial-up telephone lines, DSL, cable modem, Ethernet, Fast Ethernet
Types of networks: Local area network (LAN) and wide area network (WAN)

## Slide 51: Summary (continued)
The Internet is a huge interconnected "network of networks"
TCP/IP is the Internet protocol hierarchy, composed of five layers: physical, data link, network, transport, and application
The World Wide Web is an information system based on the concept of hypertext